## Slide 1: Towards Inertial Musculoskeletal Analysis: Effects of Sensor-to-Segment Calibration on Predicted Ground Reaction Forces
Master‘s Thesis – Felix Laufer
wearHEALTH, TU Kaiserslautern
wearHEALTH
Medicine
Industrial Ergonomics
Robotics
HCI
Intelligent
Prostheses
Rehabilitation
Sports
Sciences

## Slide 2: Motivation – Musculoskeletal Analysis
(Clinical) Motion and Gait Analysis
kinematic & kinetic motion parameters:
anatomical kinematics
ground reaction forces
joint reaction forces
muscle forces / activations
long-term goal:
flexibel & mobile body-worn system
 inertial musculoskeletal analysis
force plates
optical
markers
camera
systems
typical gait lab equipment

## Slide 3: Introduction – Musculoskeletal Analysis Pipeline
Muscle
Recruitment
motion
trajectories
(anatomical)
joint angles
net joint moments
muscle forces
or activations
Motion
Capture
Inverse
Kinematics
Inverse
Dynamics
muscular system
model
motion
sequence
dynamic body
model
skeleton model

## Slide 4: Agenda
1. Introduction  2. Methodology & CONCEPT 3. Results 4. Discussion

## Slide 5
 Optical Motion Capture + Inverse Kinematics
motion
trajectories
(anatomical)
joint angles
net joint moments
muscle forces
or activations
Motion
Capture
Inverse
Kinematics
Inverse
Dynamics
muscular system
model
motion
sequence
dynamic body
model
skeleton model
Optical vs. Inertial
Musculoskeletal Pipeline
Muscle
Recruitment

## Slide 6: Kinematic Modeling
skeleton graph (topology)
of segments and joints
basic synovial joint types
spherical: no rotational restriction
hinge: one-axis restriction
 align frames of incident segments
+ restrict rotation using Euler angles
or:
penalize ,
: joint axis, rotation
biaxial: two-axes restriction,
 not trivial in general for non-perpendicular axes (cf. thesis)
 later
common joint types in practice

## Slide 7: Anatomical Skeletons: AnyBody Full-Body Model
“Joint kinematic calculation based on clinical direct kinematic versus inverse kinematic gait models.”
Kainz et al. 2016, Journal of Biomechanics
There are various anatomical skeleton models available!
but: kinematics is only comparable among the same underlying model
use the same, detailed, anatomically correct model for all stages of the pipeline
(avoid the propagation of modeling errors through the entire pipeline!)
AnyBody skeleton model and DoFs

## Slide 8: Classical Optical Marker-Based Body Tracking
Motion
Capture
Inverse
Kinematics
 precise kinematics  optical marker-based body tracking = “golden standard”
Model Scaling
anthropometric
measurements
regression
models
scaled kinematic model
(joint-to-joint lengths)
Model Scaling
kinematic model
Inverse Kinematics
marker & motion constraints, dep. on model scaling
skeleton joint constraints, dep. on model scaling
holonomic system
q(t): joint angle trajectories

## Slide 9
 Inertial Motion Capture + Inverse Kinematics
motion
trajectories
(anatomical)
joint angles
net joint moments
muscle forces
or activations
Motion
Capture
Inverse
Kinematics
Inverse
Dynamics
muscular system
model
motion
sequence
dynamic body
model
skeleton model
Optical vs. Inertial
Musculoskeletal Pipeline
Muscle
Recruitment

## Slide 10: Comparison of Optical vs. Inertial Body Tracking
optical: markers at bony landmarks
global body reference frame
marker tracking optimization
marker placement errors
(soft tissue artifacts)
optical
markers
Inertial Measurement
Units (IMUs)
one-to-one sensor-to-segment mapping is not feasible!
detailed skeleton model is not directly IMU-trackable
inertial: sensors at segments
local inertial sensor frames
inertial multi-body tracking problem
I2S calibration errors

## Slide 11: IMU-Trackable Anatomical Skeleton (Shoulder and Spine Rhythms)
shoulder rhythm: [AC, SC] = fshoulder (GH)
spine rhythm: [SacrumPelvis, L5Sacrum, L4L5, L3L4, L3L2, L1L2, T12L1] = fspine (TP)
f (.) are linear combinations
AnyBody skeleton implements shoulder and spine kinematics as a functions of only one joint
 „shoulder & spine rhythm“ extracted from AnyBody code and implemented
GH
(AC)
(SC)
TP
green: too many DoFs
compared to IMUs
“Shoulder Rhythm Report” and “Spine Rhythm” Technical Reports, AnyBody Technology A/S

## Slide 12: IMU-Trackable Anatomical Skeleton (Arbitrary two-Axes Joint Constraint)
redundant in-between segments  shrink segments to zero length (fuse joints)
example: ankle joint
∠(APF, SEV) ~= 60 °
red: DoFs trackable in principle, but redundant in-between segment
foot
shank
fused joint
~60 °
simple, if joint axes are perpendicular:
obtain relative orientaton between incident IMUs and decompose it (Euler angles)
“On Coordinate-Free Rotation Decomposition: Euler Angles about Arbitrary Axes.” Piovan, Bullo 2012
two-axes decomposition:
with and two non-collinear axes and ,
is decomposable about iff:
 is there a rotation decomposition about „arbitrary axes“?
is a measure of the
remaining “non-decomposability“ of
 use as a joint constraint
APF
SEV

## Slide 13: Inertial Inverse Kinematics
Motion
Capture
Inverse
Kinematics
Complementary Inertial Sensor Fusion / Strapdown Integration:
accelerometer + gyroscope ( + magnetometer )
Multi Sensor Fusion: Extended Kalman Filter (EKF)
Coupled Fusion Approach: QuatTracker
tackable skeleton model
( + two-axes joint constraints
+ shoulder & spine rhythm )
QuatTracker
EKF
Strapdown
“On inertial body tracking in the presence of model calibration errors”, Miezal, Taetz, Bleser, Sensors, vol. 16, no. 7, p. 1132, 2016

## Slide 14
 Inverse Dynamics + Static Optimization
motion
trajectories
(anatomical)
joint angles
net joint moments
muscle forces
or activations
Motion
Capture
Inverse
Kinematics
Inverse
Dynamics
muscular system
model
motion
sequence
dynamic body
model
skeleton model
Optical vs. Inertial
Musculoskeletal Pipeline
Muscle
Recruitment

## Slide 15: Dynamic Modeling
dynamic body model
(masses and inertia)
+
muscular system model
(muscle geometry)
basic hill type muscle model (musculotendon unit )
scaled dynamic model
Model Scaling
body mass
distributions
body fat per-
centage (BMI)
scaled kinematic model

## Slide 16: Inverse Dynamics
Inverse
Dynamics
shoulder pitch
shoulder roll
shoulder yaw
elbow pitch
wrist yaw
wrist pitch
elbow roll
example: arm without hand
7 DoFs
but > 20 skeletal muscles
joints are over-actuated  muscle system is underdetermined
 muscle recruitment solution requires additional constraints
Muscular Redundancy Problem
- “How to distribute net joint moments over all involved muscles?”
M
M
F
F
mapping?
Equations of Motion
net forces
and torques
 muscle forces?
Muscle
Recruitment

## Slide 17: Muscle Recruitment Optimization
Inverse
Dynamics
p = 1: linear recruitment: allocate more work to stronger muscles
 minimum number of muscles for equilibrium
cf. polynomial norms
p = 2: quadratic recruitment: penalize large single force terms
 emphasize load sharing, i.e. muscle synergy effects
p = ∞: min-max recruitment: balance loads among muscles as best as possible
 minimum muscle fatigue or maximum synergism criterion
Idea of Static Optimization
in each time step, choose a solution that minimizes the total muscle stress
while fulfilling the force balance prescribed by the equations of motion:
Muscle Recruitment Criterion
Muscle
Recruitment

## Slide 18: Ground Reaction Forces
Inverse
Dynamics
Static
Optimization
Limitations of GRF Measurements
possible dynamic inconsistency of equations of motions for measured GRFs
inconvenient and inflexible force plate devices
GRF prediction using additional assumptions / constraints ... ?
  optimization based approach [Audu et al. 2003]
  smooth transitions functions, interpolated from empirical measurements [Ren et al. 2008]
  artificial neural networks [Choi et al. 2013]
  zero-moment point (robotics)
  or ... ?
Why and how to measure GRFs?
 GRFs indetermined during double feet contact phases (closed kinematic chain)

## Slide 19: Ground Reaction Force Prediction
Inverse
Dynamics
Static
Optimization
Idea: Artificial Muscle-Like Actuators at Foot Ground Contact Points
 integration into Static Optimization
25 ground contact points per foot
5 muscle-like actuators per point
ground contact conditions for each point:
  zero-velocity condition
  height threshold
“Prediction of ground reaction forces and moments during various activities of daily living.” Fluit et al. 2014, Journal of Biomechanics

## Slide 20: Agenda
1. Introduction 2. Methodology & CONCEPT  3. Results 4. Discussion

## Slide 21
 GRF Prediction: Validation & Sensitivity Analysis
Static
Optimization
motion
trajectories
(anatomical)
joint angles
net joint moments
muscle forces
or activations
Motion
Capture
Inverse
Kinematics
Inverse
Dynamics
muscular system
model
motion
sequence
dynamic body
model
skeleton model
Optical vs. Inertial
Musculoskeletal Pipeline
predicted
GRFS

## Slide 22: GRF Prediction Validation
 results in accordance with [Fluit et al. 2014] and [Skals 2016]
1
2
3
4
5
gait cycle with gait events
2
3
4
5
1
x
y
z

## Slide 23: GRF Prediction Sensitivity Analysis (Ground Contact Conditions)
 GRF prediction is robust against foot posture disturbances
tradeoff between prediction robustness
and CoP precision
Ankle Plantar Flexion (APF)
Subtalar Eversion (SEV)
APF + SEV  foot posture during touchdown
error sampling range of [±12 ° x ±12 °]

## Slide 24
 I2S Calibration Error Simulation
Static
Optimization
motion
trajectories
(anatomical)
joint angles
net joint moments
muscle forces
or activations
Motion
Capture
Inverse
Kinematics
Inverse
Dynamics
muscular system
model
motion
sequence
dynamic body
model
skeleton model
predicted
GRFS
Optical vs. Inertial
Musculoskeletal Pipeline

## Slide 25: I2S Calibration Error Simulation
segment
IMU
segment
IMU
  Effects of simulated I2S calibration errors on predicted GRFs
   how accurate are biomechanical analysis results w.r.t. I2S errors?
   what calibration precision is required?
simulated errors around lateral and segmental axes

## Slide 26: I2S Calibration Errors: Effects on Predicted GRFs per Segment
correlations of disturbed vs. true predicted GRFs for anterior initial calibration, error sampling range of [±12 ° x ±12 °]
Pelvis
Thigh
Shank
Foot
correlations of disturbed vs. true predicted GRFs for lateral initial calibration, error sampling range of [±12 ° x ±12 °]
anterior initial calibration
lateral initial calibration

## Slide 27: I2S Calibration Errors: Effects on Predicted GRFs per Segment
qualitattive correlation distributions for lateral initial calibration, error sampling range of [±12 ° x ±12 °]
Shank
Foot
seg
lat
seg
lat
Mx (fro)
Fx (ant-pos)
Fy (med-lat)
Fz (ver)
My (sag)
Mz (tra)
Mx (fro)
Fx (ant-pos)
Fy (med-lat)
Fz (ver)
My (sag)
Mz (tra)

## Slide 28: I2S Calibration Errors: Effects on Predicted GRFs in Typical Scenario
monte carlo simulation of I2S errors for all lower body segments in an error range of [±12 ° x ±12 °]
monte carlo simulation of I2S errors for all lower body segments in a reduced range of [±6 ° x ±6 °]

## Slide 29: Agenda
1. Introduction 2. Methodology & CONCEPT 3. Results  4. Discussion

## Slide 30: Conclusion
musculoskeletal analysis pipeline for both optical and inertial body tracking
anatomical IMU-trackable skeleton, consistently used in the entire pipeline
   avoid (unknown) modeling errors
integration of a universal GRF prediction approach
   “universal” = no training / empirical data required, only kinematics
sensitivity of GRF Prediction (ground contact conditions)
   very robust for moderate foot posture disturbances
systematic I2S calibration error simulation
   robustness dependent on initial IMU configuration per segment
   generally: much higher impact of errors on lateral axis
   acceptable GRF prediction errors for proper initial configuration
typical I2S error scenario for all lower body segments
   errors at segments accumulate  moderate to high GRF prediction deviations
   acceptable errors for reduced error range of [±6 ° x ±6 °]

## Slide 31: Future Work
  quantitatively proof the advantages of using the same model for the entire pipeline
     compare with kinematics + dynamics obtained with different models
  repeat studies with real data
     use real inertial reference trajectories
    use force plate measurements
  what about pathological gaits / motion sequences?
   GRF prediction valid?
  lower body  full-body I2S error simulation
  (investigate muscle activation estimations in more detail)
  (can we make the inverse dynamics computationally more efficient?)
  (integrate and compare different biomechanical frameworks and models, e.g. OpenSim vs. AnyBody)

## Slide 32
Thank you for your attention!
Questions?

## Slide 33
 Overall System Design & Implementation
Muscle
Recruitment
motion
trajectories
(anatomical)
joint angles
net joint moments
muscle forces
or activations
Motion
Capture
Inverse
Kinematics
Inverse
Dynamics
muscular system
model
motion
sequence
dynamic body
model
skeleton model
Optical vs. Inertial
Musculoskeletal Pipeline
predicted
GRFs
#include <everything>

## Slide 34: Overall Design & Implementation
I2S Trajectory Simulation
  data differentiation
  realistic inertial sensor error + noise model

## Slide 35: Shoulder Rhythm Implementation
public static Dictionary<string, EulerAngles> ShoulderRhythmDOFs(EulerAngles glenohumeralLeftDOFs, EulerAngles glenohumeralRightDOFs)
{
glenohumeralLeftDOFs = glenohumeralLeftDOFs.ToEulerAngles("XZY");
glenohumeralRightDOFs = glenohumeralRightDOFs.ToEulerAngles("XZY");
// Functions from shoulder rhythm definition in file /Body/AAUHuman/Arm/JntSR.any
var sternoClavicularLeftDOFs = new EulerAngles(
0.422 * glenohumeralLeftDOFs.X - 0.423,
-0.242 * glenohumeralLeftDOFs.X + 0.12 * glenohumeralLeftDOFs.Z + 0.851 * -0.401 - 4.983.ToRad() + 10d.ToRad(),
0.123 * glenohumeralLeftDOFs.X - 0.046 * glenohumeralLeftDOFs.Z + 0.493 * 0.201 + 3.917.ToRad() - 6d.ToRad()
, "YZX");
var sternoClavicularRightDOFs = new EulerAngles(
0.422 * glenohumeralRightDOFs.X - 0.423,
-0.242 * glenohumeralRightDOFs.X + 0.12 * glenohumeralRightDOFs.Z + 0.851 * -0.401 - 4.983.ToRad() + 10d.ToRad(),
0.123 * glenohumeralRightDOFs.X - 0.046 * glenohumeralRightDOFs.Z + 0.493 * 0.201 + 3.917.ToRad() - 6d.ToRad()
, "YZX");
var sign = +1d;
var scapulaThoraxLeftDOFs = new EulerAngles(
0d,
-0.049 * sign * glenohumeralLeftDOFs.X + 0.14 * sign * glenohumeralLeftDOFs.Z + sign * -1.203.ToRad() + 0.901 * 0.33 + 10d.ToRad(),
0.396 * sign * glenohumeralLeftDOFs.X - 0.079 * sign * glenohumeralLeftDOFs.Z + sign * 3.095.ToRad() + 0.414 * 0.307 - 10d.ToRad()
, "YZX");
sign = -1d;
var scapulaThoraxRightDOFs = new EulerAngles(
0d,
-0.049 * sign * glenohumeralLeftDOFs.X + 0.14 * sign * glenohumeralLeftDOFs.Z + sign * -1.203.ToRad() + 0.901 * 0.33 + 10d.ToRad(),
0.396 * sign * glenohumeralLeftDOFs.X - 0.079 * sign * glenohumeralLeftDOFs.Z + sign * 3.095.ToRad() + 0.414 * 0.307 - 10d.ToRad()
, "YZX");
return new Dictionary<string, EulerAngles>()
{
{ "SternoClavicularLeft", sternoClavicularLeftDOFs },
{ "SternoClavicularRight", sternoClavicularRightDOFs },
{ "ScapulaThoraxLeft", scapulaThoraxLeftDOFs },
{ "ScapulaThoraxRight", scapulaThoraxRightDOFs }
};
}

## Slide 36: Spine Rhythm Implementation
public static Dictionary<string, EulerAngles> SpineRhythmDOFs(EulerAngles pelvisThoraxDOFs)
{
pelvisThoraxDOFs = pelvisThoraxDOFs.ToEulerAngles("ZYX");
var t12L1WeightMatrix = Matrix<double>.Build.DenseOfArray(new[,]
{
// Matrix from spine rhythm definition in file /Body/AAUHuman/Trunk/SRMatrixes.any
{ 7.105616e-002, 2.276759e-001, 4.020500e-001, 5.784718e-001, 7.462112e-001, 9.131695e-001, 1.00000000000 }, // X factors
{ 0.00000000000, 1.421123e-001, 3.132395e-001, 4.908604e-001, 6.660833e-001, 8.263391e-001, 1.00000000000 }, // Y factors
{ 7.105616e-002, 2.276759e-001, 4.020500e-001, 5.784718e-001, 7.462112e-001, 9.131695e-001, 1.00000000000 } // Z factors
});
var t12L1DOFs = new EulerAngles(pelvisThoraxDOFs.X / t12L1WeightMatrix.Row(0).Sum(), pelvisThoraxDOFs.Y / t12L1WeightMatrix.Row(1).Sum(), pelvisThoraxDOFs.Z / t12L1WeightMatrix.Row(2).Sum());
return new Dictionary<string, EulerAngles>()
{
{ "SacrumPelvis" , new EulerAngles(t12L1DOFs.X * t12L1WeightMatrix[0, 0], t12L1DOFs.Y * t12L1WeightMatrix[1, 0], t12L1DOFs.Z * t12L1WeightMatrix[2, 0]) },
{ "L5Sacrum" , new EulerAngles(t12L1DOFs.X * t12L1WeightMatrix[0, 1], t12L1DOFs.Y * t12L1WeightMatrix[1, 1], t12L1DOFs.Z * t12L1WeightMatrix[2, 1]) },
{ "L4L5" , new EulerAngles(t12L1DOFs.X * t12L1WeightMatrix[0, 2], t12L1DOFs.Y * t12L1WeightMatrix[1, 2], t12L1DOFs.Z * t12L1WeightMatrix[2, 2]) },
{ "L3L4" , new EulerAngles(t12L1DOFs.X * t12L1WeightMatrix[0, 3], t12L1DOFs.Y * t12L1WeightMatrix[1, 3], t12L1DOFs.Z * t12L1WeightMatrix[2, 3]) },
{ "L2L3" , new EulerAngles(t12L1DOFs.X * t12L1WeightMatrix[0, 4], t12L1DOFs.Y * t12L1WeightMatrix[1, 4], t12L1DOFs.Z * t12L1WeightMatrix[2, 4]) },
{ "L1L2" , new EulerAngles(t12L1DOFs.X * t12L1WeightMatrix[0, 5], t12L1DOFs.Y * t12L1WeightMatrix[1, 5], t12L1DOFs.Z * t12L1WeightMatrix[2, 5]) },
{ "T12L1" , t12L1DOFs }
};
}